## Slide 1: PLANNING IN LAPEL C2 District Parking Requirements
July 2025
Prepared by: Marcellus Johnson

## Slide 2: Contents
C2 Zoning District Intent
C2 District Map (Annotated)
C2 Parking Requirements
C2 Parking Design Standards
Parking Requirements Conformity
Existing Off-Street Parking
Existing On-Street Parking
Further Recommendations
References and Further Reading

## Slide 3
The “C2”, Downtown Commercial District is intended to provide for the continued viability of the historic central business district. This district is also intended to accommodate and support the use of existing structures within the downtown. It is further intended to permit the continued, contextually appropriate, development of the area through re-use, infill, and mixed-used development.
C2 Zoning Intent

## Slide 4
C2 District Map
N <
Town Hall
State Bank
Post Office
Smoky’s
Lapel Bulldog
Includes:
28 buildings
21 businesses
11 residences
1 park
1 parking lot

## Slide 5: C2 Parking Requirements
V7.2.15. Parking Standards
    1.5 off-street spaces per dwelling unit and 1 visitor parking space for every 2 units
    1 off-street space for every employee working the longest shift (FTE)
    0.5-1 off-street space for each business vehicle on site
    0.5-1.5 off-street spaces according to square footage/seats in an auditorium or dining room

## Slide 6: C2 Parking Design Standards
V7.2.15. Parking Standards
    Parking lots must be paved and spots clearly marked with paint
    Parking spaces shall be placed so that they do not require vehicles to maneuver in a public ROW or entrance drive
    Parking lots must be fully curbed and have wheel stops as necessary
    Parking lots must have lighting and landscaping (if 6 or more spaces)

## Slide 7
N <
Town Hall
State Bank
Post Office
Smoky’s
Lapel Bulldog
Parking Requirements Conformity
Current C2 Zoning would require a minimum of 287 off-street spaces. When the required parking stall and drive aisle dimensions are included, this would amount to over 115,000 sf.

## Slide 8
N <
Town Hall
State Bank
Post Office
Smoky’s
Lapel Bulldog
Existing Off-Street Parking
Currently vacant parcels used for parking (cyan) total about 33,976 sf, which is only about 1/3 of the estimated space needed to bring all existing buildings into conformity (orange).

## Slide 9: What can be done to better align parking standards with zoning intent?

## Slide 10
N <
Town Hall
State Bank
Post Office
Smoky’s
Lapel Bulldog
Remove Off-Street Parking Minimums
On Main Street, there are already 84 marked on-street spaces with space in the rights of way on either side to add around 36 more marked and properly paved/maintained spaces.
For standard operations, existing on-street parking is sufficient to meet current demand, and it is unnecessary to require new businesses to provide additional off-street spaces.

## Slide 11: Further Recommendations
Allow on-street parking to be factored into required parking
“In lieu” fees – charge applicants for each spot they don’t provide
Fees could be set aside to fund road maintenance or maintenance of on-street parking
Loosen design standards and encourage greater use of alleys

## Slide 12: References and Further Reading
  Best Practices: Parking Management & Design. Des Moines Metropolitan Planning Organization
  Planning for Whole Communities Toolkit – Parking Management. Puget Sound Regional Council
  Parking Policy Innovations in the United States. Urban Land Institute